## Slide 1
A LOW-COST INFRARED VIDEO SYSTEM FOR REMOTE BAT COLONY MONITORING, INCLUDING RECORDS OF LITTLE BROWN BAT SYSTEMATIC SEASONAL VARIATION
              Larry Gorham, Community Scientist
              James Fischer, WMCC Wildlife Biologist
              Dr. Devaughn Fraser, CT DEEP Wildlife Biologist
              Daniela Ramirez, Student Volunteer
Notes: Good morning
I’m Larry Gorham and I’ll be discussing our low-cost IR recording system for the little brown bat maternal colony at the White Memorial Conservation Center in Litchfield, CT.
I’m a retired engineer with a passion for bats but I’m not an expert so please bare with me on the biology. I want to thank two wildlife biologists for support and guidance. James Fischer at White Memorial and Dr. Devaugh Fraser at Connecticut DEEP.
I also had help counting bats from a highly motivated high school student, Daniela Ramirez.

## Slide 2
How do we continuously video bats in the woods?
              There is
                No WiFi
                No Internet
                No electricity
              We use solar power and a battery
              Illuminate the bat houses with infrared light
              Record bat videos onto a flash drive
              Collect the data every few days

## Slide 3
Colony With
Recording System
Notes: This is the complete system, shown here securely mounted on an existing little brown bat maternal colony.
Battery box on the ground locked to the pole
Control box shoulder high
Camera/IR lights about 8 feet
And 100 watt solar panel on top
The two bat houses are just below the solar panel platform

## Slide 4
Remote Infrared (IR) Bat Recorder
            Automatic
            Remote and secure
            Powerful IR lights (850nm)
            Solar and battery powered
            All software is public domain
            Inexpensive < $700
Notes: The system is designed to be completely automatic. It can be installed remotely and be relatively secure. It uses IR lights for illumination. It is solar and battery powered. All software is public domain. And our first system that recorded last year was 700 dollars.

## Slide 5
IR Camera & Lights
Notes: Here is the camera and IR lights
The camera is a very common 40 USD security camera with a couple of minor modifications. It will do hi-res but I recorded in low-res to reduce the post processing load.
The two lights require 6 watts each and produce 850 nm IR which is invisible to bats.

## Slide 6
Remote, Solar - battery powered IR Video recording system - Approximate Cost
Camera - ELP-USBGS5MP01-V100, Global Shutter IR (Amazon) 167.00 USD
Waterproof capsule from SVPRO USB camera (Amazon) 40.00
IR Light 940nm UQISOVI (Amazon) 26.00 x 2 52.00
Computer - Raspberry Pi 4B - 2GByte (Amazon) 63.00
Smart Cooling Fan - SeenGreat PWM 33.00
Power Manager, Real Time Clock - Witty Pi 4, UUGear 58.00
USB SD drive - various 10.00
Solar Collector 100 Watts 160.00
Solar Panel Mount, Regony Home Depot 30.00
Battery, lead acid 150.00
Solar Battery controller, LiTime 20 Amp PWM Amazon 43.00
Secure System Enclosure, Steel, Vevor.com 53.00
Marine plywood platform 100.00
Hardware, electrical wire, 150.00
Tax, Shipping 100.00
Total 1209.00 USD
Notes: The system from last year was about 700 USD and that’s gone up to about 1000 USD now. This list uses a much better camera and tops out at about 1200 USD. Oddly enough one of the most expensive items is the marine grade plywood mount for the solar panel. There’s a side pole mount that’s about 1/3 the cost of a top mount. Depending on the sunlight probability a less expensive 50 watt solar panel would also work.

## Slide 7
Control Panel
Notes: This is the control panel with switches at the top, computer stack below and the orange solar controller at the bottom. The switches just isolate components, I’ll discuss the computer stack next and the solar controller provides for battery charging. The controller is a little more expensive MPPT type which provides much more efficient battery charging. The wire shown hanging out the door is an HDMI connection for a monitor so program updates can be done in the field. The panel has a locking door and is securely attached to the pole

## Slide 8
Compute Stack
Notes: The compute stack starts with a Raspberri Pi on bottom with a fan module in the middle and a WittyPi4 power controller on top. The Raspberry PI starts recording video when it is booted up but that requires about 20 watts of power so it must be shut down when not recording. The WittyPI starts and stops the Raspberry Pi according to the stored schedule. It only uses ¼ watt so the battery lasts much longer. The WittyPi always runs in the background, contains the schedule and start times for every record in the entire active season.

## Slide 9
Bat Egressing
Notes: This is a 30 sec video recorded at the maternal colony and looking at the bottom egress openings of the two bat houses. It shows a bat emerge from inside the larger bat house to “light sample” for a brief period. Then, unlike some Gen Zer’s it launches into flight. The action is slowed by a factor of 10 for this demonstration.

## Slide 10
How To Count Bats
We could stand there for two hours and watch them leave
  But that’s too difficult and it’s dark.
Instead we video the bats in infrared light
We could view the two hour video or
Use a computer to scan the video and help us count bats
ThruTracker by Dr. Aaron Corcoran of UC Colorado Springs
Notes: We could physically watch the bat house for the two hour period and count the bats but that is really difficult to get accurate results. We could record the bats ultrasonically but that method has been shown to have a wide range of counting errors. Instead we video the bats in infrared light.
Then, we could view the two hour video or
Use a computer program to scan the video and help us count bats.
We are currently using the ThruTracker software by Dr. Aaron Corcoran of UC Colorado Springs

## Slide 11
Insect Flyby
Notes: ThruTracker subtracts the static background from each frame and assigns a track to every object of a predetermined size and velocity. This slide demonstrates the problem with using IR illumination. This is an insect track that must be ignored. If we used a 1500 dollar thermal camera only bats and a few birds would be tracked. The IR method is more labor intensive but less expensive. With this method every track must be viewed and classified. ThruTracker also has automatic counting features that are being fine tuned for the next version.

## Slide 12
Bat Flyby
Notes: This slide shows a bat track that can easily be classified as a flyby event because it never comes close to either bat house. This is all very interesting but we want to know which bats are actually egressing and returning to the bat house.

## Slide 13
Bat Egressing
Notes: This slide shows a bat egressing the larger bat house. ThruTracker also designates where the track starts and ends so it is easy to determine whether the bat is egressing or returning.

## Slide 14
Net Outflow = Egress - Returns
Chart: 
NET OUTFLOW
Notes: We subtract the bats returning from the bats egressing to get the Net Outflow number. This is sometimes called Residents since it appears that number slept in the bat house that day. This slide shows the Net Outflow for each day through out the active season with about 5% data losses. This recovering colony shows a maximum over 300 bats with wide day to day variation.

## Slide 15
Chart: 
Egress Start Time (Min from sunset)
MINUTES FROM SUNSET
Notes: This plot shows a systematic seasonal trend in the bat egress start times measured in minutes from sunset. The bats egress about 20 minutes after sunset in mid summer and about 35 minutes after sunset in spring and fall. This phenomena has been reported previously in many species. One theory is that the pregnant and lactating females are much more stressed in summer and must egress earlier to attain the needed calories.

## Slide 16
Comparing Net Outflow (blue) and Flyby Activity (orange)
Chart: 
| 45807 | 45808 | 45809 | 45810 | 45811 | 45812 | 45813 | 45814 | 45815 | 45816 | 45817 | 45818 | 45819 | 45820 | 45821 | 45822 | 45823 | 45824 | 45825 | 45826 | 45827 | 45828 | 45829 | 45830 | 45831 | 45832 | 45833 | 45834 | 45835 | 45836 | 45837 | 45838
Flyby | 154 | 138 | 408 | 548 | 1184 | 1254 | 1814 | 1683 | 1472 | 464 | 384 | 229 | 27 | 88 | 72 | 75 | 64 | 24 | 1373 | 533 | 266 | 439 | 239 | 66 | 61 | 86
Net Outflow | 279 | 283 | 273 | 264 | 227 | 214 | 194 | 51 | 110 | 231 | 250 | 247 | 284 | 291 | 220 | 263 | 306 | 304 | 234 | 83 | 99 | 134 | 218 | 309 | 286 | 203
FLYBYS
NET OUTFLOWE
Notes: This slide shows another interesting bat behavior that occurred in June. The orange plot shows the number of bat flyby’s and the blue plot shows the Net Outflow all recorded for each day. Except for those 6 days lost due to a disk crash. It’s interesting that the flyby numbers rise to a peak and then fall around our estimate of Parturition and around Volency. If this phenomena could be substantiated then it could be used to identify when Parturition and Volency occure.

## Slide 17
GitHub QR Code
Notes: Finally As previously mentioned this project is registered public domain so the QR code above will go directly to the GitHub site. It contains all computer code and a wiki with extensive construction notes and system test scripts. You can snap a picture of this or I have a short handout summarizing the project.